TH38D16S  Module Wiring Manual

Ver 1.0

Contents

1. Function Brief	1

2. Main Interface of TH38D16S	2

2.1 TH38D16S Interface Diagram	2

2.2 Pin Definition of TH38D16S Interface Board’s Functional Interfaces	2

3. Appendix: Basic Connection	3

3.1 DIP1 Power Port	3

3.2 DIP1 Network Interface	3

3.3 DIP2 Audio Input, Audio Output	5

3.4 DIP3 Lamp board control interface	5

3.5 DIP5 Extended function interface	6

# 1. Function Brief

If you need personalized IP camera products, board level network video module is your best choice. It is easy for you to manufacture personalized IR IP camera, you just need to open camera housing, fix the network video module and connect them.

# 2. Main Interface of TH38D16S

## 2.1 TH38D16S Interface Diagram

Veneer behind Interface Figure    Veneer front Interface Figure

## 2.2 Pin Definition of TH38D16S Interface Board’s Functional Interfaces

DIP1：Power Input and Network Interface

| 1 | DC12V |
| --- | --- |
| 2 | GND |
| 3 | Rx- |
| 4 | Rx+ |
| 5 | Tx- |
| 6 | Tx+ |
| 7 | ACT+ |
| 8 | ACT- |

DIP2：Audio Input, Audio output interface

| 1 | Audio output: (effective value)） |
| --- | --- |
| 2 | Audio input: (effective value) |
| 3 | GND |

DIP3：Smart interface

| 1 | Light board alarm signal output |  |
| --- | --- | --- |
| 2 | Light board fill control signal output |  |

DIP4: IR-CUT Interface

| 1 | IR-CUT connection port 1 |
| --- | --- |
| 2 | IR-CUT connection port 2 |

DIP5：Extended function interface

| 1 | 3.3V |
| --- | --- |
| 2 | Audio power amplifier control signal output |
| 3 |  |
| 4 |  |
| 5 | GND |

# 3. Appendix: Basic Connection

## 3.1 DIP1 Power Port

## 3.2 DIP1 Network Interface

Example 1: Method of directly connect to network cable

Example 2: Use crossover cable connect to PC through RJ45 socket

## 3.3 DIP2 Audio Input, Audio Output

Audio Output：Load impedance R, Power P, P=1000/R

| R | P |
| --- | --- |
| 32Ω | 30mw |
| 16Ω | 62mw |

## 3.4 DIP3 Lamp board control interface

## 3.5 DIP5 Extended function interface

# Text boxes

1  2 3 4 5 6 7 8

DIP1

12V power supply

12V

GND

Orange-white

Green

Orange

3  4  5  6  7  8

DIP1

6

3

2

1

Network connect status indicator light

Green-white

1.TX+

2.TX-

3.RX+

4.NU

5.NU

6.RX-

7.NU

8.NU

RJ45 Pin

3  3  5  6  7  8

DIP1

Crossover Cable

1  2  3

DIP2

Audio Output

Audio Input

GND (Audio)

12v   GND

Connect the light board alarm light control interface

1  2

Output Intelligent Signal Control Lamp Board Lighting

1  2  3  4  5

Connect to the audio power amplifier control board signal input interface